## Slide 2: INTRODUCTION
PCBs → Heart of every electronic device (mobile, laptop, car, satellite)
Even small manufacturing defects → Device failure + High cost + Safety risk
Traditional methods have serious limitations:
Manual inspection → Slow, tiring, human error
Rule-based AOI → High false positives, misses
tiny/complex defects
Growing need for:
Fast & accurate defect detection
Precise location (not just yes/no)
Clear visual output for operators
Project Goal: Build intelligent automated system using Deep Learning (YOLOv8) + Web Interface

## Slide 3: Problem Statement & Motivation
PCBs are critical → defects cause failures, cost, safety risks
Common defects: Missing Hole, Mouse Bite, Open Circuit, Short, Spur, Spurious Copper
Limitations
Manual inspection → slow, inconsistent
Rule-based AOI → high false positives, misses
subtle defect
Need: Accurate localization + real-time visual feedback

## Slide 4
Missed_Holes Mouse_Bites Open _Circuites
Shorts Spur Spurious_Copper

## Slide 5: Objectives
Prepare dataset from DeepPCB using subtraction & ROI extraction
Train high-accuracy object detection model (YOLOv8)
Build simple web app for upload → detect → download annotated results
Visual: Bullet icons + small flowchart teaser

## Slide 6: Methodology
System Architecture

## Slide 7: Milestone 1 – Dataset Preparation
Dataset: DeepPCB (template-defect pairs)
Module 1: Image subtraction
Grayscale → Resize (1/4) → Gaussian Blur → Adaptive Threshold →
Subtract → Otsu
Module 2: Contour detection & ROI crop
Find contours → Filter area 1–300 → Crop 64×64 around centroid

## Slide 8
→
→
→
→

## Slide 9: Grey Scale Patches
Missing_Hole Mouse_Bite Open_Circuit
Short Spur Spur_Copper

## Slide 10: Milestone 2 – Model Training & Evaluation
Switched from EfficientNet to YOLOv8n (for efficient detection accuracy)
Steps:
Combine patches → XML → YOLO labels → Train/val/test split
Train: 80 epochs, batch 16, imgsz=640
Model is applied to individual/new images → generate predictions, visualize results, compute per-image metrics

## Slide 11: YOLO Training Process
Data Preparation + Augmentation
Model configuration is done as YOLOv8n/s/m/l/x + epochs=80, batch=16, imgsz=640
Model enters Training Loop repeats the below process till completion of training round (epoch) forward → loss → backward → optimizer → repeat.
Validation after epochs/Training round mAP calculation on val set → early stopping possible
Final Evaluation performed on following metrics Mean Average Precision , Precision, Recall, F1-score

## Slide 12
Evaluation:
Test set metrics:
Test mAP@0.5 : 0.8390 ← Primary accuracy metric (Mean Average Precision)
Test Precision (mean) : 0.8811
Test Recall (mean) : 0.7476
Test F1-score (mean) : 0.8040

## Slide 15: Milestone 2 – Test Inference
Load data from every defect class in random manner
Load the trained YOLOv8 model to perform inference on the selected test images
Run YOLOv8 inference on each test image to generate defect predictions
Draw red bounding boxes and labels on the original images, overlay predictions, and save the visualized results.
Save all annotated images

## Slide 16: Detected Images
Missing_Hole Mouse_Bite Open_Circuit

## Slide 17: Detected Images
Short Spur Spur_Copper

## Slide 18: Milestone 3 : Web Application – Streamlit UI
Streamlite UI is for frontend web application
Upload PCB image (.jpg/.png)
Real-time YOLOv8 detection
Side-by-side: Original vs Annotated
Defect table (class + confidence)
Download annotated image
Style: Thick red boxes (width=10), large bold white labels with black outline

## Slide 19: Results

## Slide 20: Conclusion
Built end-to-end automated PCB defect detection system
Overcomes drawbacks of manual inspection & rule-based AOI
Integrated YOLOv8 nano → accurate localization & classification of 6 defects: Missing Hole, Mouse Bite, Open Circuit, Short, Spur, Spurious Copper
Switched from EfficientNet → better small/subtle defect detection
Achieved test mAP@0.5 > 0.83
Streamlit web app: real-time upload, thick red boxes + bold labels, downloadable results
Practical for industrial quality control
Demonstrates strong fusion of computer vision, deep learning & deployment

## Slide 21: Future Scope
Support for full-size PCB images (sliding window / tiling inference)
Integration of template-test pair upload
Mobile/edge deployment (YOLOv8 export to ONNX / TensorRT)
Addition of more defect classes (e.g., solder joint issues)
Active learning pipeline for continuous model improvement using factory data
Cloud deployment with user authentication and report generation